## Slide 1
Bolt
Machine :
MDX-540A & ZCL-540
  No T-Slot Table
Materials Required:
White Acetal/Delrin Material (US-SRP-DEL)
  5.0” x 3.0” x 1.0”
0.125 Ball End Mill (EMB-125-3F-125)
0.063 Ball End Mill (EMB-125-3F-063)
0.031 Ball End Mill (EMB-125-3F-031)
0.125(3.175mm) Collet
SRP Player Software
Post Clean up :
Hack saw to cut part out
600 Grit sand paper to clean ends of bolt (available @ home depot)
Special Notes:
You may have to move the X-Origin to the right of the material more to avoid the clamp. Start the machine and set the feed rate to 10% and check the clearance as it runs.